## Slide 1: Social Distancing in Education
April 17, 2020
Notes: Social distancing, or physical distancing, is a set of non-pharmaceutical interventions or measures taken to prevent the spread of a contagious disease by maintaining a physical distance between people and reducing the number of times people come into close contact with each other. Wikipedia

## Slide 2
Social Distancing Design Considerations
SOCIAL DISTANCING IN EDUCATION
Spatial Considerations
Spatial Considerations
Consider recommended mandates when designing classrooms which vary by state, city, region, and district and may change daily so solutions should be flexible and agile to morph as current guidelines are updated.
Consider the impact of social distancing to manage infectious diseases in the classroom and the reality that class sizes will likely be reduced in the near term.
Consider 6’ spacing between students initially to comply with CDC recommendations which may be reduced as the threat relaxes.
Consider fewer transitions into different learning modes to minimize active interactions during this time of heightened sensitivity.
Consider ways to enable visual connections between learners, instructor and content to enhance student engagement.
Consider removing the instructor desk/podium or turn it away from students to reduce the threat of transmissions.
Consider wider pathways and unidirectional flow in and out of the building, classroom, corridors, breakout in-between spaces to give more distance between students as they travel through the school.
Social distancing, or physical distancing, is a set of non-pharmaceutical interventions or measures taken to prevent the spread of a contagious disease by maintaining a physical distance between people and reducing the number of times people come into close contact with each other. Wikipedia
Notes: Social distancing, or physical distancing, is a set of non-pharmaceutical interventions or measures taken to prevent the spread of a contagious disease by maintaining a physical distance between people and reducing the number of times people come into close contact with each other. Wikipedia
Suggested requirements are changing daily as the condition intensifies and will continue to change as the thread is reduced over time.

## Slide 3
SOCIAL DISTANCING IN EDUCATION
SAME CLASSROOM WITH 6’ SOCIAL DISTANCING
19 students
TYPICAL CLASSROOM BEFORE SOCIAL DISTANCING
36 students
28’6” x 34’11” = 976 SF
Plan Views
Remove chairs at existing classroom tables to allow for social distancing of 6’ between students. Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people (as shown on right), then bring all 36 chairs back when conditions fully recover.
Classroom A | Before & During Social Distancing
SAME CLASSROOM WITH 3’ SOCIAL DISTANCING
29 students

## Slide 4
SOCIAL DISTANCING IN EDUCATION
GROUP BREAKOUT MODE
PRESENTATION MODE
28’6” x 34’11” = 976 SF
36 students = 27 SF per student
Plan Views
Classroom A | Before Social Distancing
Typical active learning classroom layout.

## Slide 5
Classroom A | Before Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
36 students = 27 SF per student
Presentation Mode
Typical active learning classroom layout.

## Slide 6
Classroom A | Option A with Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
36 students = 27 SF per student
Presentation Mode
Typical active learning classroom layout using Verb Personal Whiteboards as a quick social distancing measure.

## Slide 7
Classroom A | Option B | 6’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
19 students = 51 SF per student
Presentation Mode
Remove chairs at existing tables to allow for 6’ social distancing.

## Slide 8
Classroom A | Option C | 3’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
29 students = 34 SF per student
Presentation Mode
Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people, then bring all 36 chairs back when conditions fully recover.

## Slide 9
Classroom A | Before Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
36 students = 27 SF per student
Group Breakout Mode
Typical active learning classroom layout.

## Slide 10
Classroom A | Option B | 6’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
19 students = 51 SF per student
Group Breakout Mode
Remove chairs at existing tables to allow for 6’ social distancing.

## Slide 11
Classroom B | Varying Levels of Social Distancing
SOCIAL DISTANCING IN EDUCATION
SAME CLASSROOM
WITH 3’ SOCIAL DISTANCING
21 students
SAME CLASSROOM
WITH 6’ SOCIAL DISTANCING
16 students
28’6” x 34’11” = 976 SF
21 students = 46 SF per student
Plan Views
Remove chairs at existing tables to allow for social distancing. Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people (as shown), then bring all 33 chairs back when fully recovered.
TYPICAL CLASSROOM
NO SOCIAL DISTANCING
33 students

## Slide 12
Classroom B | 6’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
16 students = 61 SF per student
Presentation Mode
Remove chairs at existing tables to allow for social distancing. Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people (as shown), then bring all 30 chairs back when fully recovered.

## Slide 13
Classroom B | 3’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
28’6” x 34’11” = 976 SF
21 students = 46 SF per student
Presentation Mode
Remove chairs at existing tables to allow for social distancing. Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people (as shown), then bring all 30 chairs back when fully recovered.

## Slide 14
Classroom B | 6’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
Group Breakout Mode
28’6” x 34’11” = 976 SF
16 students = 61 SF per student
Remove chairs at existing tables to allow for social distancing. Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people (as shown), then bring all 30 chairs back when fully recovered. .

## Slide 15
Classroom B | 3’ Social Distancing
SOCIAL DISTANCING IN EDUCATION
Group Breakout Mode
28’6” x 34’11” = 976 SF
21 students = 46 SF per student
Remove chairs at existing tables to allow for social distancing. Add chairs as restrictions relax to achieve a more relaxed spacing of 3’ between people (as shown), then bring all 30 chairs back when fully recovered. .

## Slide 16
Classroom C | Individual Tables w/ Freestanding Separation Screens
SOCIAL DISTANCING IN EDUCATION
PRESENTATION MODE
28’6” x 34’11” = 976 SF
18 students = 54 SF per student
Plan Views
GROUP BREAKOUT MODE
This scenario provides additional protection between students with plexiglass Freestanding Separation Screens.
As a result, student count is reduced from 30 to 18 students.

## Slide 17
Classroom C | Individual Tables w/ Freestanding Separation Screens
SOCIAL DISTANCING IN EDUCATION
Presentation Mode
28’6” x 34’11” = 976 SF
18 students = 54 SF per student
This scenario provides additional protection between students with plexiglass Freestanding Separation Screens.
As a result, student count is reduced from 30 to 18 students.

## Slide 18
Classroom C | Individual Tables w/ Freestanding Separation Screens
SOCIAL DISTANCING IN EDUCATION
Group Breakout Mode
28’6” x 34’11” = 976 SF
18 students = 54 SF per student
This scenario provides additional protection between students with plexiglass Freestanding Separation Screens.
As a result, student count is reduced from 30 to 18 students.

## Slide 19
In-Between Focus Spaces

## Slide 20
In-Between Spaces | Brody Desk & Lounge
SOCIAL DISTANCING IN EDUCATION
Individual Micro-Environment
Separate Brody in a student commons setting, them replace them adjacent when social distancing restrictions relax.
Without Social Distancing.
With Social Distancing.

## Slide 21
In-Between Spaces | Brody Desk & Lounge
SOCIAL DISTANCING IN EDUCATION
Individual Settings
Provide a variety of individual settings where students can study, focus and rejuvenate alone at a safe distance from others.

## Slide 22
Love How You Learn

## Slide 23
Appendix

## Slide 24
Classroom D | Large Lecture Hall
SOCIAL DISTANCING IN EDUCATION
Presentation Mode
64’8” x 62’6” = 976 SF
64 students = 63 SF per student
Density in a lecture hall is significantly reduced, but will allow for chairs to be added as the threat lessens.

## Slide 25
Social Distancing Design Considerations
SOCIAL DISTANCING IN EDUCATION
Guideline Examples
Images may have copyright restrictions.
Notes: Social distancing, or physical distancing, is a set of non-pharmaceutical interventions or measures taken to prevent the spread of a contagious disease by maintaining a physical distance between people and reducing the number of times people come into close contact with each other. Wikipedia
Suggested requirements are changing daily as the condition intensifies and will continue to change as the thread is reduced over time.

## Slide 26
Social Distancing Guidelines
SOCIAL DISTANCING IN EDUCATION
Poster Examples
Images may have copyright restrictions.
Notes: Social distancing, or physical distancing, is a set of non-pharmaceutical interventions or measures taken to prevent the spread of a contagious disease by maintaining a physical distance between people and reducing the number of times people come into close contact with each other. Wikipedia